## Slide 1: Frequency And Sound Recognition on the Micro:bit V2
Joshua Hill

## Slide 2: Pipeline
…
…
…
…
Normaliser
Splitter
Level Detector
…
Frequency Detector
Tap Recogniser
Morse Code
Mic Recorder
…
Microphone

## Slide 3: Frequency Detection Base Design
Core Audio Processor Functionality – Recognise up to
Two frequencies and their closest Note Letter
Frequency Detector
Splitter
Frequency in Hz
Closest Note
On Note Heard

## Slide 4: Frequency Detection Base Implemented
Core Audio Processor Functionality – Recognise up to
Two frequencies and their closest Note Letter
Get Closest Primary note
Get Primary Frequency
Get Closest Secondary Note
Get Secondary Frequency
On Hearing (Note)
Start
Stop
Char / Int
Int
Char / Int
Int
Event e
Void
Void
CPP / MakeCode Adaptation
Frequency Detector
Splitter

## Slide 5: Sine vs Square
Sine waves are easier to detect – they produce a peak at the relevant bin and frequency is simply bin resolution * bin number with highest magnitude.
Square waves are more complex, the base frequency is actually the distance between the harmonic spikes on the graph

## Slide 6: What does a Micro:bit Wave look like?
Spikes not always evenly distanced, not in correct order of magnitude
Spike at resonant frequency of speaker which is ~2700hz

## Slide 7: Recognition Accuracy
Results across the board are within 2.6hz of the target frequency, with average difference of just 0.7hz

## Slide 8: FFT Statistics
2048 size FFT
Bin resolution of 11,025/2048 = 5.38hz
Runs on a 128 byte (sample) sliding window, doing 2 FFT runs per input buffer from the mic (256 samples)
Takes ~10-11ms to run at most (if square wave detection is required)

## Slide 9
Event Based Detection – showing closest primary note

## Slide 10
Primary and Secondary Frequency Test
Format:
P—P
Primary Note
Primary Frequency
S—S
Secondary Note
Secondary Frequency

## Slide 11
Primary and Secondary Frequency Visual Test Left primary, Right secondary

## Slide 12: HTTP request/response – showing distance effect on signal strength

## Slide 13: How noise (literally!) disrupts signals

## Slide 14: Morse Code
Capable of converting strings into Morse dots and dashes
Can play and detect in two frequencies simultaneously (primary and secondary)
Optimized for 30cm distance
Audio Processor
CPP / MakeCode Adaptation
Morse Code
Play Char
Play String
Serial Print Stored
Get Last Char
Get Stored Message
Clear Stored Message
Start
Stop
Void
Void
Void
Char / Int
String
Void
Void
Void

## Slide 15: Morse Features
No sync needed – attempts to do it on the fly by adjusting its run time between each sample slightly (primary freq only).
Number correct needed configured when Micro:bits are 30cm apart.

## Slide 16
We actually have 22-23 samples per frame for a 250ms dot length, and 44 for a 500ms dot length.
Real threshold based on testing from 30cm away – less than half to account for the off failed recognition

## Slide 17
500ms Morse Test 30cm
Starting 0 means – nothing recieved

## Slide 18
250ms Morse Test 30cm

## Slide 19
Voice Morse Test
A
B and C

## Slide 20: Tap Detector
Intro to ML + Pattern Detection
Record and store Patterns (up to 10), each bin accounts for 500ms
Test live input for matches to stored patterns
Audio Processor
CPP / MakeCode Adaptation
Tap Detector
Record Pattern
Redo Pattern
On Pattern Recognised
Void
Void
Event e

## Slide 22
Tap recogniser test
Pattern recorded by pressing A
Print out format
Ans | Live input | Stored Pattern | Euclidean distance
Final Euclidean distance shown at bottom of each segment
Buffers should be read bottom to top i.e. most recent value last
Pattern hummed in binary is:
Non-exact match found
1 | 33
0 | 0
1 | 32
0 | 0
1 | 44
1 | 44
1 | 17
0 | 0
0 | 0
0 | 0

## Slide 23: uBit initialised + Auto run on function calls (don’t need to call fft->startRecording)

## Slide 24: Events